| POWER ON DEVICE |
| --- |
| Plug device into wall and flip the power switch on the back of the device to the ON position and wait till fan activates. Press and hold the button for 2 seconds until you hear an audible beep. |
| POWER OFF DEVICE |
| Press and hold the button for 2 seconds until you hear an audible beep. Screen will become blank. Flip the power switch on the back of the device to the OFF position, fan will stop running. |
| COLD OR COLD/COMPRESSION THERAPY |
| Start Cold Press the COOL button Let circulate for 1 minute Temperature can be adjusted using the ↕ Start Compression Press the COMP button Pressure can be increased by tapping the COMP button | Manual Stop Cold Press and hold the COOL button for 2 seconds Manual Stop Compression Press the COMP button and cycle through all settings until compression turns off *Cold and Compression therapy will automatically turn off after prescribed session length is reached |
| DVT THERAPY FOR THE CALF OR FOOT |
| Start DVT Press the DVT button *Cold and Compression therapy will automatically turn off after prescribed session length is reached | Manual Stop DVT Press the DVT button |
| PAD SHOULD BE APPLIED TO PATIENT PRIOR TO STARTING THERAPY |
| HEAT THERAPY |
| Start Heat Press the HEAT button *Heat will automatically turn off after prescribed session length is reached | Manual Stop Press and hold the HEAT button for 2 seconds |
| CONTRAST THERAPY |
| Start Contrast Press and hold the COOL and HEAT button simultaneously Temperature can be adjusted using the ↕ Pressure can be increased by tapping the COMP button | Manual Stop Press and hold the COOL and HEAT button for 2 seconds *Therapy will automatically turn off after prescribed session length is reached |
| IF ALARM SOUNDS | WARNINGS |
| If Screen Shows “CHECK WRAP, CHECK WATER LEVEL” Check that the wrap is fully connected to the proper fittings on back of unit Check for kinks in the wrap hose, and straighten hose Check liquid level in reservoir. Add liquid if below Min. line Run the therapy for several minutes with the cap removed from the reservoir to allow any air that may have become trapped to escape from the system | Heat Do not use heat unless prescribed |
|  | CONTRAINDICATIONS |
|  | Cold therapy should not be used by persons with Raynaud’s disease or any other peripheral vascular disorder, cold hypersensitivity or compromised circulation. |